## Slide 1
https://inst.eecs.berkeley.edu/~cs188/fa18/

## Slide 2
Goal: optimize building energy consumption and cost
Develop algorithm to learn electrical patterns and optimize building energy consumption or cost
Test two algorithms: DQL and DPG. Novel gradient method to allow DPG to handle multiple actions
Reduce load peaks and minimize cost of energy
For DQL, discretized continuous states for each state dimension: 2048 discrete states
In general, RL cannot handle continuous states and has to discretize them
Matrix of Q-values is stored in memory – thus the only option is to store them using NN

## Slide 3
Multiple buildings
Two main categories of loads: flexible and fixed consumption
  Within flexible loads: three types
  Time-scaling load (e.g. HVAC, television, fridge, lights): Can be switched on-off for a limited number of times
  Time-shifting load (e.g. dishwasher): Must consume a minimum amount of power over time interval. Cannot be interrupted for a series of time steps
  Both (e.g. electric vehicle):
Two tariffs: Cost of buying from utility; cost of selling to utility
Goal: minimize earnings from selling – cost from buying
Flexible loads are either on or off
All loads are greater than zero
Tariffs are all greater than zero
PV is non-curtailable
Our model has large continuous state space: Building energy consumption and price at every time t
Action space: dependent on electric device constraints

## Slide 4
First we built an environment game
In this game, for each day we didn’t alter the base load
For flexible loads, we evaluated each possibility and game it a reward based on how it did against our optimization goal
We didn’t optimize the existing off-line database
After training it on an off-line database, it can be used in an on-line environment
If the on-line environment has changed from the training environment, the model can learn these changes and adapt
Each state is encoded in the DNN input at a time interval of 2 steps
  For peak reduction problem, input layer has 11 neurons:
    Timestep t
    Base load at t
    PV at t
    AC at t
    EV at t
    Dishwasher at t
    PV at t+1
    AC at t+1
    EV at t+1
    Dishwasher at t+1

## Slide 5
We assume that PV and base load are fixed, the others change based on the learning process
Number of layers and neurons in each layer were chosen based on trial and error
3 hidden layers, each with 100 neurons with ReLU activation function
For DQN, the output layer has 8 neurons, each representing Q-value for combine action
  AC off / EV off/ Dishwasher off
  AC on / EV off / Dishwasher off
  AC off / EV on / Dishwasher off
  AC off / EV off/ Dishwasher on
  AC on / EV on / Dishwasher off
  AC on / EV off / Dishwasher on
  AC off / EV on / Dishwasher on
  AC on / EV on / Dishwasher on
Learning rate = 0.1
Discount factor = 0.99
N = 0.01 (for ReLU)
Model trained for 5000 episodes, where an episode is composed by 20 randomly chosen days
Weights update performed after every 2 episodes
Reward function computed at the end of the day, instead of each time step
Reward function penalizes lots of switching